## Slide 1
Improving the throughput of veterinary drug residue analysis using vibrational shaking technology
Dr Martin Danaher
Food Safety Department,
Teagasc Food Research Centre, Ashtown, Dublin, Ireland.

## Slide 2
Teagasc (chaw-gask) Research
- 300 research projects
500 scientific and technical staff and ~ 100 postgraduate research
students (MSc, PhD) in collaboration with Irish universities
8 Research centers across the country
      Agriculture
      1. Dairy & pig production
      3. Beef production
      4. Crops
      Sheep production
      Environment
      Food
      7. Ashtown, Dublin
      8. Moorepark, Cork

## Slide 3
Why Monitor for residues in food?
Exposure to high concentrations of veterinary drug residues through food consumption can potentially impact on human health, especially vulnerable individuals
  Neonates
  Pregnant women
  Other sensitive groups
Examples of undesirable toxic effects
  Teratogenic/Embryotoxic - Anthelmintics
  Neurotoxic – Ivermectin/Pyrethroids
  Allergic reaction - Penicillins

## Slide 4
Agri-food is Irelands largest indigenous industry
Employs 150,000 people
Annual value of €24 billion
Beef and livestock sector (€1.9 billion)
Ireland is the second largest producer and exporter of infant milk formula
Brand Reputation: Food island “green” image
Compliance with EU Legislation
Economics

## Slide 5
Food producing species

## Slide 6
Analytical matrices

## Slide 7: Bioanalytical methods

## Slide 8: Trends in Residue Analysis
Pre-2008 lower throughput 24 samples per day.
Post-2008 methods implemented 50 samples per day
  Move from HPLC-UV/FLD or GC-ECD to LC-MS/MS or GC-MS(/MS)
  Development of high throughput generic sample preparation methods e.g. QuEChERS.
Since, exponential improvement in MS technology, allowing analytical separation to be compressed.
Desirable to improve the detection of non-compliant results by analysing more samples but this is limited by challenges in sample preparation.

## Slide 9: QuEChERS Approach
Phase Separation
D-SPE
Analysis
Concentration
4g MgSO4 + 1g NaCl
1.5g MgSO4 +
0.5g C18
6 mL Supernatant +
0.5 mL DMSO

## Slide 10: QuEChERS Extraction
Probe homogenisation (30 sec).
Clean probe (60 sec).
Total time = 54 min (for 36 samples).
Add salts.
Shake samples (60 sec).
Total time = 6 min.

## Slide 11: Limitations of QuEChERS
Six samples can be only shaken at a time:
  Otherwise you can get clumping of salts and poor dispersion of the sample.
Insufficient shaking of samples can lead to lower extraction efficiency and inconsistent results.
The samples need to be blended or prehomogenised.

## Slide 12: Probe based extraction
Disperses sample and increases contact with solvent.
30-60 sec 18000 rpm.
Effective and efficient
Low throughput, one sample at a time.
Requires cleaning of probe between samples.
Ice bath required for volatile or thermally labile analytes.

## Slide 13: Ceramic Homogenisers
Reported application in QuEChERS by Rothermich, Agilent Technologies at EPRW 2010.
Reduces shaking time from 60 sec to 20 sec.
Breaks up MgSO4 and NaCl clumps during QuEChERS extraction of veterinary drug residues from animal tissue.
Improved and more consistent recovery.

## Slide 14: Automated shaking
Ceramic homogeniser pellets are added to samples.
Salts are added to samples at same time.
Samples (n = 36) are placed in the shaker in the test tube racks (n = 3).
Rack is clamped.
Samples are shaken at 700 rpm.
Instrument shaking time is adjusted to give the desired extraction efficiency.

## Slide 15: Vibrational Extraction System
Start/Stop button
Emergency stop
Operating light
Shaking speeds
Clamp
Electronic door locking

## Slide 16: Research questions
How does this extraction approach compare to the standard probe based extraction?
How does it work with naturally incurred samples?
Will the approach reduce sample preparation time in the laboratory?
Notes: For this I would show four rack for muscle and liver both with and without.

## Slide 17: Experimental Results

## Slide 18: Shaker vs Probe (Liver tissue)
10 g bovine liver samples extracted with 12 mL ACN
4 min
0 min
8 min
2 min
Probe
30 sec

## Slide 19: Shaker vs Probe (Muscle tissue)
10 g sample extracted with 12 mL ACN
4 min
0 min
8 min
2 min
Probe
30 sec

## Slide 20: QuEChERS Extraction
Liver Samples (manual)
Muscle Samples (manual)
P
P
C
C
P
P
C
C
Liver Samples (Shaker)
Muscle Samples (shaker)
C
C
C
C
P
P
P
P

## Slide 21: Standard vs New Method
P
C
P
C
Liver
Muscle
Liver
Muscle

## Slide 22: Incurred bovine liver study
Chart: Concentration (ppb)
| Albendazole | Albendazole-sulphoxide | Albendazole-sulphone | Albendazole-amino-sulphone | Fenbendazole | Oxfendazole | Fenbendazole-sulphone | Levamisole | Clorsulon | Oxyclozanide | Rafoxanide | Ivermectin B1a | Triclabendazole | Triclabendazole-sulphoxide | Triclabendazole-sulphone | Levamisole
Probe Homogeniser | 203 | 107 | 277 | 153 | 712 | 149 | 85 | 149 | 590 | 132 | 181 | 167 | 1954 | 94 | 651 | 259
Vibrational Shaker | 200 | 105 | 286 | 152 | 668 | 158 | 84 | 155 | 608 | 173 | 174 | 170 | 1939 | 84 | 682 | 257

## Slide 23: Incurred bovine muscle study
Chart: Concentration (ppb)
| Albendazole | Albendazole-sulphoxide | Albendazole-sulphone | Albendazole-amino-sulphone | Fenbendazole | Oxfendazole | Fenbendazole-sulphone | Levamisole | Clorsulon | Oxyclozanide | Rafoxanide | Ivermectin B1a | Triclabendazole | Triclabendazole-sulphoxide | Triclabendazole-sulphone | Levamisole
Probe Homogeniser | 63 | 10 | 42.4 | 24.1 | 147 | 46.6 | 113 | 315 | 14.3 | 32.8 | 7 | 3 | 95 | 13.1 | 168 | 273
Vibrational Shaker | 60 | 9.4 | 41.9 | 21.5 | 162 | 43.5 | 144 | 322 | 14.6 | 32.5 | 7.3 | 2.9 | 96 | 14.3 | 156 | 258

## Slide 24: QuEChERS Extraction
Comparison
Probe method >60 min.
Shaker 13 min.
Time saving of 47 min for 36 samples
8 min
5 min

## Slide 25: Anticcoccidials in meat

## Slide 27: HILIC Separation
LC-MS/MS Set-Up B
Kinetex 2.6 μm Hilic100A 100 x 2.1 mm
MPA: 50mM Ammonium Formate + 0.1% Formic
MPB: MeCN + 0.1% Formic
Column Temp: 50 C
Injection Volume: 2.5 μL
TIME (MIN) | %A | %B
Initial | 5 | 95
1.50 | 5 | 95
2.00 | 50 | 50
3.10 | 50 | 50
3.20 | 5 | 95
4.50 | 5 | 95
Hilic Gradient

## Slide 28: RP-UHPLC Separation
LC-MS/MS Set-up A
Acquity UPLC BEH C8 1.7µm, 2.1x50 mm Column
MPA: H2O +0.1% Formic
MPB: MeCN + 0.1% Formic
Flow Rate: 0.6 mLmin-1
Column Temp: 60 C
Injection Volume: 2.5 µL
TIME (MIN) | %A | %B
Initial | 100 | 0
2.00 | 100 | 0
2.10 | 83.3 | 16.7
3.50 | 83.3 | 16.7
3.90 | 55.5 | 44.5
5.00 | 55.5 | 44.5
5.50 | 33.5 | 66.5
9.00 | 33.5 | 66.5
9.10 | 0.0 | 100
11.10 | 0.0 | 100
11.20 | 100 | 0
13.20 | 100 | 0
C8 Gradient

## Slide 29: MS/MS overview
C8 acquisition
HILIC acquisition

## Slide 30: Sample preparation overview
Weigh 5g meat
Homogenise, 1 min; Vortex 1 min
Shake, 20 min @ 200 rpm
Centrifuge, 10 min, 3500 rpm, 4 C
Add 20 mL of MeCN (Pest)
N2-Evap. 10 mL
Reconstitute, 80:20 v/v MeCN:H2O
Filter, 0.2 μm PTFE
LC-MS/MS Analysis
Weigh 5g meat
Vibrational shaker 8 min.
Centrifuge, 10 min, 3500 rpm, 4 C
Add 20 mL of MeCN (Pest)
N2-Evap. 10 mL
Reconstitute, 80:20 v/v MeCN:H2O
Filter, 0.2 μm PTFE
LC-MS/MS Analysis

## Slide 31: Fortified chicken muscle study
Chart: Anticoccidials from Muscle Tissue: Vibrational Shaking vs Probe Homogenisation
| Clopidol | Diaveridine | Aprinocid | Ethopabate | Robenidine | Tolt-So2 | Nicarbazin | Nequinate | Tolt-So | Diclazuril | Tolt | Decoquinate | Semduramicin | Monensin | Lasalocid | Salinomycin | Laidlomycin | Maduramycin | Narasin | Cyromazine | Halofuginine | Amprolium | Imidocarb
Probe | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
Minimix (5 min) | 96.9287 | 95.9323 | 95.5776 | 95.6649 | 92.3715 | 96.3523 | 109.792 | 99.5997 | 95.9397 | 99.7503 | 94.9704 | 118.1699 | 108.524 | 90.6575 | 75.8779 | 80.4722 | 88.0467 | 83.0589 | 90.5868 | 101.6505 | 83.8938 | 131.3147 | 95.1992
Minimix (8 min) | 98.1126 | 98.7251 | 95.3066 | 94.4313 | 91.347 | 97.3922 | 104.9193 | 102.2639 | 95.3056 | 101.621 | 95.0114 | 148.8154 | 136.462 | 92.4977 | 85.2439 | 76.7377 | 93.3773 | 80.413 | 87.1409 | 106.5872 | 110.7312 | 182.9349 | 97.5288

## Slide 32: Anticoccidials result summary
Higher response with shaker for amprolium, decoquinate and semduramicin,
 | Recovery (%) | 
Analyte | Shaker (5 min) | Shaker (8 min)
Amprolium | 131 | 183
Decoquinate | 118 | 149
Semduramicin | 109 | 136
Results summary overall
Precision | Probe | Shaker (5 min) | Shaker (8 min)
<10% | 15 | 16 | 14
10-23% | 7 | 7 | 7
>23% | 1 (lasalocid) | 1 (Amprol.) | 2 (Amprol. & Lasal.)
Notes: For this I would show four rack for muscle and liver both with and without.

## Slide 33: Conclusions
Vibrational shaking in combination with ceramic homogenisers gives comparable disruption to probe homogenisation.
Results with incurred tissue is comparable for the analytes tested, better in some cases.
Because disruption is carried out in a closed tube the risk of cross-contamination of samples during sample preparation is low.
The approach significantly improves sample throughput in the laboratory.
Possible to achieve more output with the same resources.
Notes: For this I would show four rack for muscle and liver both with and without.

## Slide 34: Acknowledgements
Teagasc Walsh Fellowship programme for funding this research.
Teagasc Staff for conducting experiments, processing data and help in preparing this presentation.
Acknowledge in particular: Sarah Tuck, Damien Mooney, Cormac McElhinney, Conor Lavelle and Mary Moloney.